## Slide 1: Aibo Open R Introduction
AJ Ureel

## Slide 2: Outline
Architecture
Class Development
Hello World Example
Example 2
Competitor Code
Conclusions & Next Steps
Sources
Q & A

## Slide 3: Architecture
3 Layer Architecture
Hardware
Services
Application
Notes: Layered structure of the software and services provided by the system layer
The OPEN-R system layer provides a set of services (input of sound data,
output of sound data, input of image data, output of control data to joints, and
input of data from various sensors) as the interface to the application layer.
This interface is also implemented by inter-object communication.
These services enable application objects to utilize the robot’s underlying
functionality, without requiring detailed knowledge of the hardware devices that
comprise the robot.
The system layer also provides the interface to the TCP/IP protocol stack,
which enables programmers to create networking applications utilizing the
wireless LAN.

## Slide 4: Architecture Hardware
Hardware
  CPU
  Power System
  Sensors
  Devices
    Actuators (Motors)
    Speakers
    Lights
  Memory Stick
  Wireless Device

## Slide 5: Architecture Application
“Object” Driven
  Objects (Executables) are loaded upon boot up.
  Executables typically have the “.bin” extension.
  Objects communicate via messaging.
Notes: The use of inter-object communication enables each object to be created separately
and later be connected to other objects. This results in a very efficient development
lifecycle.
When two objects communicate, the side that sends data is called the “subject,” and
the side that receives data is called the “observer”. The subject sends a
‘NotifyEvent’ to the observer. NotifyEvent includes the data that the subject wants to
send to the observer. The observer sends a ‘ReadyEvent’ to the subject. The purpose
of ReadyEvent is to inform the subject that the observer is ready to receive data or
not. If the observer is not ready to receive data, the subject does not send any data to
the observer.

## Slide 6: Architecture Object Messaging
Object Communication
  Subject - Observer

## Slide 7: Class Development
Class Characteristics
Basic Methods
Communication Methods
Class Development Steps

## Slide 8: Class Dev. Class Characteristics
A core class inherits from the OObject class.
A core class implements
  DoInit()
  DoStart()
  DoStop()
  DoDestroy().
A core class has the necessary number of OSubject and OObserver.
  numOfSubject and numOfObserver are defined in def.h that is generated by the stubgen2 command.
Notes: A core class is a C++ class that represents an object. Each object should be
represented by only one core class.
Objects have entry points for receiving messages. Each
entry point corresponds to a particular method of the object, and each method
corresponds to a particular member function of the core class.

## Slide 9: Class Dev. Basic Methods
Init method
  This is called at startup. This method initializes instances and variables.
Start method
  This is called at startup after Init is executed in all objects.
Stop method
  This is called at shutdown.
Destroy method
  This is called at shutdown after Stop is executed in all objects. This method destroys the subject and observer instances.
Notes: These methods are called during startup and shutdown.
The Init method, Start method, Stop method, and Destroy method
correspond to each DoInit(), DoStart(), DoStop() and DoDestroy() function
in the object’s corresponding core class, respectively.

## Slide 10: Class Dev. Communication Methods
Methods used in subjects:
  Control method This receives the connection results between the subject and its observers.
  Ready method The subject receives ASSERT-READY or DEASSERT-READY notifications from the observers.
Methods used in observers:
  Connect method This receives the connection results between an observer and its subjects.
  Notify method This receives a message from the subject.
Notes: These methods have the following characteristics.
(a) The member functions corresponding to Control methods, Ready
methods, Connect methods, and Notify methods are described in
stub.cfg.
(b) The member functions receiving a message are described in stub.cfg, but
it is not necessary to describe the member functions sending a message
in stub.cfg.

## Slide 11: Class Dev. Class Development Steps
(1) Design your objects
(2) Design the data type for inter-object communication
(3) Description of stub.cfg
(4) Implementation of a core class
(5) Decide the configuration of your .ocf file
(6) Build
(7) Edit the setting files
(8) Execution on AIBO
(9) Debugging
Notes: What is a Stub file?
The Stub file defines the connection between an object’s entry points and it’s corresponding core class member function.
What is an OCF file?
The OCF provides the object’s runtime configuration and is in the format:
object OBJECT_NAME STACK_SIZE HEAP_SIZE SCHED_PRIORITY CACHE TLB MODE
What are Settings files?
.CFG files. There are 3: Object (Objects to be executed), Connect (Definition of inter-object connectivity), and DesignDB (list od files and paths accessed at run-time).

## Slide 12: Hello World
Wireless Console
Code
Compiling
Memory Stick
Results
Notes: SDK Example

## Slide 13: Hello World Wireless Console
WLAN Manager vs. WConsole
  WLAN Manager allows for creation of WLanConf.txt & access to Aibo Mind http pages.
  WConsole is used for debugging and system monitoring.
DLink Setup
  Success achieved with static IP address.

## Slide 14: Hello World Code
Directory Structure & Files
  C:\cygwin\usr\local\MyProj\common\HelloWorld\HelloWorld

## Slide 15: Hello World Code
HelloWorld.h
#ifndef HelloWorld_h_DEFINED
#define HelloWorld_h_DEFINED
#include <OPENR/OObject.h>
class HelloWorld : public OObject {
public:
HelloWorld();
virtual ~HelloWorld() {}
virtual OStatus DoInit (const OSystemEvent& event);
virtual OStatus DoStart (const OSystemEvent& event);
virtual OStatus DoStop (const OSystemEvent& event);
virtual OStatus DoDestroy(const OSystemEvent& event);
};
#endif // HelloWorld_h_DEFINED

## Slide 16: Hello World Code
Hello
World.cc
#include <OPENR/OSyslog.h>
#include "HelloWorld.h"
HelloWorld::HelloWorld ()
{ OSYSDEBUG(("HelloWorld::HelloWorld()\n"));}
OStatus
HelloWorld::DoInit(const OSystemEvent& event)
{ OSYSDEBUG(("HelloWorld::DoInit()\n"));
return oSUCCESS;}
OStatus
HelloWorld::DoStart(const OSystemEvent& event)
{ OSYSDEBUG(("HelloWorld::DoStart()\n"));
OSYSPRINT(("!!! Hello World !!!\n"));
return oSUCCESS;}
OStatus
HelloWorld::DoStop(const OSystemEvent& event)
{ OSYSDEBUG(("HelloWorld::DoStop()\n"));
OSYSLOG1((osyslogERROR, "Bye Bye ..."));
return oSUCCESS;}
OStatus
HelloWorld::DoDestroy(const OSystemEvent& event)
{ return oSUCCESS;}
Notes: Note the 4 basic (required) methods and there are no message methods.

## Slide 17: Hello World Compiling
Go to directory and enter “make install”
Notes: Proper Stub Files, OCF, and Makefile are essential. When they are correct, compiling is a breeze.
Note: Also compiled PowerMon.Bin

## Slide 18: Hello World Memory Stick
First Copy OPEN_R_SDK\OPEN_R\MS_ERS7\WCONSOLE\memprot\OPEN-R
Then Copy HelloWorld\MS\OPEN-R
Then create your WLanCONF.txt file and copy/place on memory stick.

## Slide 19: Hello World Results

## Slide 20: Hello World Results

## Slide 21: Hello World Results
Note the additional line on power-down.

## Slide 22: Ball Tracking Head

## Slide 23
class BallTrackingHead7 : public OObject {
public:
BallTrackingHead7();
virtual ~BallTrackingHead7() {}
OSubject* subject[numOfSubject];
OObserver* observer[numOfObserver];
virtual OStatus DoInit (const OSystemEvent& event);
virtual OStatus DoStart (const OSystemEvent& event);
virtual OStatus DoStop (const OSystemEvent& event);
virtual OStatus DoDestroy(const OSystemEvent& event);
void NotifyResult(const ONotifyEvent& event);
void NotifyImage(const ONotifyEvent& event);
void NotifySensor(const ONotifyEvent& event);

## Slide 24: Ball Tracking Head

## Slide 25: Competitor Code
German Code
  Excellent Setup
  Very Complex
  Specialized
NU Code
  A bit simpler in comparison
  NU to rewrite for 2005
    One significant factor was robot positioning (transition from offense to defense)

## Slide 26: Conclusions & Next Steps
There is a lot of information available, but much is either overly generic or very specific.
SDK Tutorials and samples are fairly good.
Need to determine if WConsole can be operated in DCHP environment.
Next Steps:
  Install TinyFTP for remote uploading of Objects
  Create custom object
    Focus on Stub, OCF, and Inter-Object Communication
  Compile and run NU code
Notes: The tutorial tends to jump from non-continuous specific example to abstract samples. It would be better to have one continuous example with abstracts interjected as needed for expanded detail. After reading the tutorial, a full understanding of the sample code is not achieved.

## Slide 27: Sources
Open R SDK: ProgrammersGuide_E.pdf
Open R SDK: InstallationGuide_E.pdf
GT-install.zip
NU: Product_Submit2004.zip
NUbotFinalReport2004.pdf
Chien-Tai (Jason) Lo: Research on AIBO ERS-7 for RoboCup soccer (http://ltu164.ltu.edu/aibo/)

## Slide 28
Q & A